## Slide 1: NLC STEM Club UAV Project
Electrical Team - First Meeting
February 2026

## Slide 2: Meeting Agenda (60 Minutes)
Project Overview & Mission (5 min)
Electrical Architecture Decision (15 min)
Power Budget & Analysis (10 min)
Safety Protocols (Mandatory) (10 min)
Subsystem Assignments (10 min)
Week 1-2 Action Plan (5 min)
Hands-On: Component Inventory (5 min)

## Slide 3: UAV Project Overview
Mission: Fixed-wing environmental monitoring UAV
  Temperature, humidity, pressure, air quality sensors
Timeline: 10 weeks total (Week 1 now)
Budget: $508 total project cost
Parts Status: All flight components arrived
  ⚠ Need to order: External 5V 6A UBEC
Team Structure: 4 electrical subsystems

## Slide 4
Key Electrical Components
• OVONIC 4S LiPo Battery (14.8V, 2200mAh)
• FLASH HOBBY D2830EVO Motor (1000KV)
• 40A ESC with 5V 3A BEC
• 4× ES08MA II Servos (metal gear)
• MATEK F405-WMN Flight Controller
• BN-220 GPS Module
• ELRS ExpressLRS Receiver
• Arduino Nano (research payload)
• BME280 Sensor (temp/humidity/pressure)
• MQ135 Gas Sensor (air quality)
• MicroSD Module (data logging)
• External 5V 6A UBEC (to order)

## Slide 5: ⚡ Critical Decision: Power Architecture
Challenge: Single BEC cannot handle servo stall + flight systems
  ESC BEC: 5V @ 3A
  4 servos can draw >3A when stalling
Failure Mode: Brownout crashes flight controller
RECOMMENDED: Dual-BEC Configuration (Option B)
  Rail 1 (ESC BEC 3A): Flight-critical systems only
  Rail 2 (External UBEC 6A): Servo power only
  Isolation prevents servo issues from crashing FC

## Slide 6
Dual-BEC Architecture (Option B)
4S LiPo (14.8V, 2200mAh) │ ┌───────────┴───────────┐ │ │ 40A ESC External UBEC (5V 3A BEC) (5V 6A) │ │ Rail 1 (3A) Rail 2 (6A) │ │ ┌───┴────┐ ┌──────┴──────┐ │ │ │ │ FC GPS Servo #1 Servo #2 Arduino ELRS Servo #3 Servo #4 ✓ Isolated power domains ✓ No single point of failure ✓ 78% margin on Rail 1, 88% on Rail 2

## Slide 7: Power Budget Analysis
5V Rail 1 (Flight-Critical, ESC BEC 3A):
  Flight Controller: 250mA
  GPS Module: 60mA
  ELRS Receiver: 90mA
  Arduino + Sensors: 263mA
  TOTAL: 663mA → Margin: 78% ✓
5V Rail 2 (Servo Power, External UBEC 6A):
  4× Servos idle: 40mA
  4× Servos moving: 720mA typical, 1200mA peak
  TOTAL: 720mA → Margin: 88% ✓

## Slide 8: ⚠ SAFETY PROTOCOLS (MANDATORY)
LiPo Battery Safety:
  Never charge unattended
  Use LiPo-safe bag or metal container
  Storage: 3.8V per cell (not full charge)
  Damaged/puffy battery = FIRE HAZARD
Propeller Safety:
  NEVER test motor indoors
  Remove prop for bench testing
  Outdoor tests: 10ft clear radius
ALL members must sign Safety Protocol acknowledgment

## Slide 9: Electrical Subsystems (4 Teams)
1. Power Team
  Battery, BECs, power distribution, current monitoring
2. Flight Electronics Team
  Flight controller, GPS, receiver, servo configuration
3. Research Payload Team
  Arduino, sensors (BME280, MQ135), data logging
4. Integration & Testing Team
  System validation, current measurements, troubleshooting

## Slide 10: Subsystem 1: Power Team
Scope: Battery → Distribution → All power rails
Week 1 Priorities:Create battery charge log spreadsheet
  Label battery with purchase date
  Measure actual battery voltage (digital multimeter)
  Design ESC mounting & cooling
Week 2 Deliverables:
  Dual-BEC system assembled on test bench
  Current monitoring functional (FC analog input)
  Power-up checklist created

## Slide 11: Subsystem 2: Flight Electronics
Scope: FC + GPS + Receiver + Servos
Week 1 Priorities:
  Install iNav or ArduPilot configurator software
  Flash firmware to MATEK F405-WMN
  Bind ELRS receiver to transmitter
  Verify GPS lock (outdoor test, >6 satellites)
  Create servo channel mapping spreadsheet
Week 2 Deliverables:
  All 4 servos responding to transmitter inputs
  GPS navigation functional (position hold mode)
  Blackbox logging enabled

## Slide 12: Subsystem 3: Research Payload
Scope: Arduino + Sensors + Data Logging
Week 1 Priorities:
  Install Arduino IDE & required libraries
  Wire BME280 sensor (I2C) and verify readings
  Start MQ135 burn-in (24-48 hours required)
  Test MicroSD module (write/read test file)
  Design data logging format (CSV headers)
Week 2 Deliverables:
  All sensors reading simultaneously
  Data logging to SD card at 1Hz
  Toggle switch control functional

## Slide 13: Subsystem 4: Integration & Testing
Scope: System validation and troubleshooting
Week 1 Priorities:
  Component inventory (verify all parts arrived)
  Identify missing items (External UBEC)
  Create wiring quality checklist
  Multimeter training (voltage, current, continuity)
  Organize component storage bins
Week 2 Deliverables:
  Measure actual current draw of all components
  Verify power budget calculations (compare to measured)
  Test BEC voltage under load
  Create troubleshooting decision tree

## Slide 14
Team Milestones: Weeks 1-2
• Week 1 Goals:
• Order External 5V 6A UBEC
• Complete component inventory
• Firmware installed on FC
• GPS verified (satellite lock)
• ELRS receiver bound
• Sensors reading (Arduino)
• Safety training completed
• Week 2 Goals:
• Dual-BEC system on bench
• All 4 servos responding
• Data logging functional
• Current measurements complete
• System integration started
• Bench test passed
• Ready for airframe integration

## Slide 15: 🔥 CRITICAL ACTION ITEMS
TODAY (Before leaving):
  Vote on Dual-BEC architecture
  Assign 4 subsystem teams
  Sign Safety Protocol acknowledgment
  Complete component inventory
WITHIN 24 HOURS:
  Order External 5V 6A UBEC (Amazon: 'Hobbywing UBEC 5V 6A')
  Set up team communication (Discord/Slack)
THIS WEEK:
  Complete all Week 1 subsystem tasks
  Weekly check-in meeting (1 hour)

## Slide 16: Meeting Documentation
Comprehensive documentation package:
  Power Budget Analysis (10 pages)
  Electrical System Block Diagram (7 pages)
  Detailed Wiring Diagram (16 pages)
  Safety Protocol (11 pages) - Signature required
  Subsystem Assignments (20+ pages)
All files available in project folder:
  STEM-electrical/
Reference these throughout the build process

## Slide 17
Questions?
Discussion

## Slide 18
Let's Build Something Incredible
NLC STEM Club UAV Project
Electrical Team - February 2026